## Slide 1: Improving Black Carbon Measurements in Ethiopian Aerosols
Ahmad Jalil
Dr. Ann M. Dillner - Dr. Hossein Kazemian
FTIR Group Seminar - June 30, 2025

## Slide 2: Research Motivation
Black Carbon measurement uncertainty:
Different methods can give vastly different results
Lack of standardized MAC values:
10 m²/g is widely used but may not be universally appropriate
Ethiopian context:
Unique aerosol composition (dust, biomass burning) challenges standard approaches
Climate relevance:
BC is the second strongest climate forcer after CO₂
Core Problem:
How do we reconcile different BC measurement techniques and derive reliable, site-specific calibrations?
Why This Work Matters

## Slide 3: Research Questions
Method Agreement:
How do raw aethalometer, HIPS (10 m²/g MAC), and FTIR-EC measurements compare at Ethiopian sites?
Optimal MAC Values:
What seasonal and wavelength-dependent MAC values minimize bias for HIPS and aethalometer when referenced to FTIR-EC?
Drivers of Variability:
How do EC composition, PM₂.₅ composition, and meteorological factors explain day-to-day MAC variations?
Transferability:
Under what conditions can site-specific MAC values be applied elsewhere without significant bias?

## Slide 4: Three Measurement Approaches
FTIR-EC:
Principle: Direct measurement of carbon bonds via IR spectroscopy
Advantage: Established reference method for elemental carbon
Sampling: 24-hour integrated
HIPS
Principle: Light absorption at 633nm + MAC conversion
Advantage: Direct optical measurement
Sampling: 24-hour integrated
Challenge: MAC variability
Aethalometer
Principle: Multi-wavelength light attenuation
Advantage: Real-time, source discrimination
Sampling: 1-minute resolution
Challenge: Filter loading effects

## Slide 6: The MAC Problem - Four Different Calculation Methods
Method 1 - Mean of Ratios:
𝑀𝐴𝐶=𝑚𝑒𝑎𝑛(𝐹_𝑎𝑏𝑠/𝐸𝐶)=11.15" " 𝑚^2/𝑔
Method 2 - Ratio of Means:
𝑀𝐴𝐶=(〖𝑚𝑒𝑎𝑛(𝐹〗_𝑎𝑏𝑠))/(𝑚𝑒𝑎𝑛(𝐸𝐶))=10."09 " 𝑚^2/𝑔
Method 3 - Standard Regression:
𝐹_𝑎𝑏𝑠=𝑚∗𝐸𝐶+𝑏→𝑀𝐴𝐶=4.20" " 𝑚^2/𝑔
Method 4 - Origin Regression:
𝐹_𝑎𝑏𝑠=𝑚∗𝐸𝐶→𝑀𝐴𝐶=9."18 " 𝑚^2/𝑔
Method 1 - Mean of Ratios:
Method 2 - Ratio of Means:
Method 3 - Standard Regression:
Method 4 - Origin Regression:
Statistical Performance vs Physical Reality:
Method 3 has the best R² (0.754) but predicts negative BC when Fabs = 0
This violates the fundamental physical constraint that zero absorption should equal zero BC.

## Slide 9: Why R² Alone Isn't Enough
The Problem with Traditional Metrics
  Pearson r²:
    Measures linear association, always positive
  Regression R²:
    Can be negative when model performs worse than mean
  Bias matters:
    Systematic over/under-estimation
  Physical constraints:
    BC = 0 when = 0
Our Approach:
  Focus on RMSE and bias rather than correlation for method selection

## Slide 10: Iron Interference Investigation
Why Iron Matters
Iron absorbs light at 633nm (HIPS wavelength)
Ethiopia has significant dust sources
Could create "false" BC signal
Average Fe concentration: ~300 ng/m³
Extinction Coefficients:
Iron (Fe³⁺): 2,220 M⁻¹ cm⁻¹
Manganese: 50-500 M⁻¹ cm⁻¹
Iron is 5-10× stronger absorber

## Slide 13: Maybe Iron isn't that bad?
Overall trend: Weak downward relationship between iron concentration and HIPS MAC
  r = -0.208, suggesting minimal direct iron effect
Critical insight: When data is separated by Ethiopian seasons (static definition), trends within each season flatten
  Dry season: MAC values consistently higher (~13 m²/g), regardless of iron levels
  Belg season: Intermediate MAC values (~10.5 m²/g), weak iron dependence
  Kiremt season: Lower MAC values (~8.5 m²/g), minimal iron trend

## Slide 14: Cross-Method Validation
FTIR-EC vs Aethalometer
Correlation: r2 = 0.608
Systematic offset: Aethalometer consistently higher
Bias: ~2× overestimation by aethalometer
HIPS vs Aethalometer
Correlation: r2 = 0.558
Similar bias pattern: Aethalometer systematically high
Temporal consistency: All methods track same events
Key Finding: Systematic Aethalometer Bias
Magnitude: Aethalometer mean = 7.7 μg/m³
FTIR/HIPS: Both ~4.6 μg/m³
Implication: Default aethalometer corrections inappropriate for this site
Possible causes: Filter loading, MAC assumptions, baseline corrections
Critical Insight:
Underlying factor causing systematic aethalometer overestimation needs investigation

## Slide 16: Key Takeaways
Method Selection Matters
Statistical performance (R²) can be misleading. Physical constraints and bias are more important for operational measurements.
Seasonality is Real
MAC values vary by >50% between dry and wet seasons.
Aethalometer Systematic Bias
Aethalometer consistently overestimates BC by ~2× compared to FTIR-EC and HIPS. This suggests default corrections are inappropriate for Ethiopian aerosols.
Site-specific Calibration Required
Universal MAC values (10 m²/g) and default instrument corrections are insufficient for accurate BC measurements in diverse environments.

## Slide 17: Next Steps
Immediate Priorities
Dynamic season definitions: Use rainfall data instead of calendar months
All wavelength analysis: Complete aethalometer multi-λ comparison
Validation with raw attenuation: Compare τ vs corrected BC
Future Directions
Pasadena comparison: Test transferability to different environment
Humidity corrections: Account for RH effects on optical measurements
Dynamic MAC: Develop dynamic MAC based on composition

## Slide 18: Acknowledgment
Supervision & Guidance
Dr. Ann Marie Dillner (UC Davis)
Dr. Hossein Kazemian (UNBC)
Collaborators
SPARTAN Network Team
NASA JPL
Addis Ababa University